## Slide 1
Bridging Eclipse SDV
for ADAS Diagnostics
Eclipse SDV Hackathon 2026
S-CORE • OpenSOVD • X-Verse • openDuT

## Slide 2
The Problem
Eclipse S-CORE
Safety Middleware
✕
Eclipse OpenSOVD
Diagnostics REST API
These projects don't work together.
Epic #1766: Diagnostics & Fault Management
Open for 1 year — Unanswered
1/10

## Slide 3
Our Solution
S-CORE
BRIDGE
PR #16
OpenSOVD
Four Contributions
01
PR #16
sovd_adapter bridge
02
Issue #553
8 API compliance fixes
03
CDA #543
Bug fix for merge
04
Demo
Cruise Control + openDuT
2/10

## Slide 4
Full Architecture with X-Verse
■ Our Code ■ X-Verse □ Upstream
Dashboard :8080
HTML/JS/Python
OpenSOVD Gateway :7690
Rust/Axum + Issue #553 Fixes
sovd_adapter (PR #16)
DataProvider | FaultProvider
cruise_diag
DTC U0100
cruise_bridge
TCP :7700
X-VERSE CONTAINER
Cruise Control Team
gatewayd
mw::com | TCP :7700
someipd
vSomeIP 3.6.1
cruise_control_main (C++)
PID Controller (Kp=0.25, Ki=0.03, Kd=0.12) | 50ms loop | mw::com Skeleton
car_simulation (C++)
Vehicle Physics | Speed Sensor | vSomeIP Publisher (Service 0x1234)
SOME/IP
TCP :7700
openDuT Testing
Distributed Test Orchestration | 13 Assertions PASS
Data Flow
Car Sim → SOME/IP → someipd
→ gatewayd → cruise_control
→ cruise_bridge → cruise_diag
→ sovd_adapter → OpenSOVD
→ Dashboard
3/10

## Slide 5
Use Case: Speed Signal Loss
Safety-Critical ADAS Scenario • ISO 26262 ASIL B
1
NORMAL
120 km/h
Cruise ON
2
FAULT
Signal Lost
Inject
3
DETECT
100ms
Timeout
4
CONFIRM
5000ms
DTC U0100
5
DISABLE
Safe
Decel
6
DIAGNOSE
REST API
/faults
Why This Use Case?
→ Safety-Critical
Without speed data, ACC cannot function safely
→ Full Stack Demo
Car Sim → X-Verse → Bridge → SOVD → Dashboard
→ Real Automotive
Actual scenario OEMs face in production
→ Shows All Projects
S-CORE + OpenSOVD + openDuT working together
4/10

## Slide 6
Scope Declaration
★ OUR CODE
→ sovd_adapter (PR #16) — ~900 lines
→ Issue #553 fixes — ~770 lines
→ cruise_diag — ~500 lines
→ cruise_bridge — ~400 lines
→ Dashboard — ~800 lines
→ CDA #543 bug fix — ~230 lines
Total: ~3,870 lines
○ X-VERSE / UPSTREAM
→ cruise_control — Cruise Team
→ car_simulation — Cruise Team
→ gatewayd — X-Verse (S-CORE)
→ someipd — X-Verse (vSomeIP)
→ OpenSOVD server — Upstream
→ openDuT framework — Upstream
Our Contribution
We built the bridge (sovd_adapter) between Eclipse S-CORE and Eclipse OpenSOVD,
fixed 8 API compliance issues, and demonstrated it with a safety-critical Cruise
Control use case running on the X-Verse deployment from the Cruise Control team.
5/10

## Slide 7
Technical Highlights
Standards Compliance
→ ISO 17978-3 — SOVD REST API
→ ISO 14229-1 — DTC Status Bits
→ ISO 26262 — ASIL B Safety
Key Implementation
→ Rust + Tokio async runtime
→ mw::com Proxy/Skeleton pattern
→ TCP bridge to X-Verse gatewayd
50ms
Control Loop
5s / 2s
Debounce
13/13
Tests Pass
~3,870
Lines
Languages: Rust • C++ • Python • HTML/JS
6/10

## Slide 8
Live Demo
00:00
Normal Operation
Dashboard: Speed=120, State=ACTIVE, Faults=0
00:15
Fault Injection
Click button → Speed signal lost
00:30
Diagnosis
curl /faults → DTC U0100 confirmed
00:45
Recovery
PUT /restart → System recovers
Dashboard • curl (REST) • X-Verse Logs • Test Results
7/10

## Slide 9
Impact
For OEMs
→ Build ADAS on Eclipse S-CORE
→ ISO 17978-3 compliant diagnostics
→ Standard REST APIs
→ No vendor lock-in
For Eclipse SDV
→ Projects work together
→ Real ADAS use case proven
→ Answers Epic #1766
→ Blueprint for integrations
Ready for Merge
PR #16 • Issue #553 • CDA #543 • Demo • Tests
8/10

## Slide 10
We bridged the gap.
Let's merge it.
S-CORE ←→ X-Verse ←→ OpenSOVD ←→ openDuT
Thank You
9/10